## Slide 1: ROW Engineering Training
Hosted by Region 3
January 14th, 2026

## Slide 2: TRAINING GOALS
To provide a high-level understanding of the ROW and Design delivery processes.
To provide a more detailed understanding of how a ROW Engineer functions within the ROW and Design delivery processes.

## Slide 3: TRAINING AGENDA ITEMS
Review Essential Responsibilities
Overview of the PDN and Overall Delivery Processes
Line and Grade
  Reviewing Plans
  Checking Title Reports
Functional Design
ROW Exhibits
Legal Descriptions
Plan Revisions
Plan-in-Hand, PS&E
Excess Land Revisions

## Slide 4: Housekeeping
Breaks to be provided, as necessary.
Please hold questions for designated Q/A.

## Slide 5: Position Responsibilities

## Slide 6: Position Qualities

## Slide 7: Position Qualities
“Ensure projects have sufficient proposed ROW while identifying and mitigating ROW risks.”

## Slide 8: PROJECT DELIVERY NETWORK
Project Delivery Network (PDN)

## Slide 9: ROW PROCESS FLOWCHART
Design Guidelines - PDN

## Slide 10: Line and Grade

## Slide 11: ROW Engineer’s Goals (L&G)
Help the project team establish the ROW footprint for the project.
  Identifying ROW impact risks and high-risk tracts
  Reviewing access management
  Reviewing constructability
Ensuring properties are shown in their most current conditions.
  Property boundaries
  Improvements
  Septic Systems

## Slide 12: ROW Engineer’s Goals (L&G)
Help keep the project within:
  Scope
  Schedule
  Budget

## Slide 13: ROW Engineering Resources
TDOT Standard Drawings
TDOT Design Guidelines
TDOT Highway Safety Access Manual
TDOT Driveway Manual
TDOT Standard Spec Book for Road and Bridge Construction
TDOT Design Checklists
AASHTO Greenbook and AASHTO Roadside Design Guide
PROWAG
Tennessee Property Viewer Website and other County Websites

## Slide 14: REVIEWING PLANS AS A ROW ENGINEER

## Slide 15: Example of Review Item
RD11TS4.pdf
RD11TS3A.pdf

## Slide 16: Example of Review Item
SEPTIC SYSTEMS SHOULD BE LOCATED. HIGH RISK IMPACT.

## Slide 17: Example of Review Item
STUDY ACCESS MANAGEMENT

## Slide 18: Example of Review Item
STUDY ACCESS MANAGEMENT

## Slide 19: Example of Review Item
NEED FOR PROP. ROW FOR PROP BRIDGE ABUTMENT.

## Slide 20: Checking Title Reports
The most current owner name and deed reference for each tract should be included in the roadway plans.
It’s important to check the title reports for:
  Plats
  Existing Easements (need to be shown in the plans!)
  ROW Dedications
  Other documents which might affect acquisition

## Slide 21: Checking Title Reports
COUNTY WEBSITES AND THE TN PROPERTY VIEWER AID IN CHECKING PROPERTY BOUNDARIES

## Slide 22: Checking Title Reports
PLANS (LEFT) VS. PLAT (RIGHT) – SURVEY UPDATE REQUIRED

## Slide 23: Functional Design
Functional Design

## Slide 24: Functional Design
Project Delivery Network (PDN)

## Slide 25: ROW Engineer’s Goals (FD)
Ensure ROW acquisition is appropriate for the project.
  Identifying ROW impact risks and high-risk tracts
  Reviewing access management
  Reviewing constructability
Ensuring properties are shown in their most current conditions.
  Ownership Information Matches the Title Reports
  Property boundaries
  Improvements

## Slide 26: ROW Engineer’s Goals (FD)
Help keep the project within:
  Scope
  Schedule
  Budget

## Slide 27: Reviewing Functional Design Plans
Design Should be Completed
  More focused review of ROW impacts on each tract
  Checking for sufficient ROW for
    EPSC
    Traffic Control
    Constructability
    Drainage

## Slide 28: Reviewing Functional Design Plans
(See HP checklist)

## Slide 29: Example of Review Item
CONTEXTUAL ENTRANCE DESIGN
FROM HSAM

## Slide 30: Example of Review Item
SMALL GRAVITY RETAINING WALL (STD. DWG. W-SG-1) COULD PREVENT IMPACTS
WSG1.pdf

## Slide 31: Example of Review Item
ENSURE SUFFICIENT CONST. ESMT FOR EPSC

## Slide 32: Example of Review Item
PROJECTS WITHOUT ROW ACQUISITION SHOULD STILL BE REVIEWED FOR ROW IMPACTS (DRAINAGE) AND DESIGN COMPLIANCE
(From PROWAG)

## Slide 33: ADDITIONAL FUNCTIONAL DESIGN ACTIVITIES
Uploading the ROW Acquisition table to IRIS
Attend Preliminary Group Inspection (PGI)
  Visit the project with the ROW team and assist appraisers in developing their PGI report
  Recommend hosting a Pre-PGI meeting to review a KMZ of the project before going out in the field
Attend public meetings

## Slide 34: ROW Exhibits
Per IB 25-10, TDOT design guidelines contain guidance for ROW Exhibit creation on ORD
  Guidance is available for MicroStation at R3
ROW Engineer is to provide Quality Control checks on ROW Exhibits

## Slide 35: ROW Exhibits
(Review Example)

## Slide 36: LEGAL DESCRIPTIONS
ROW Engineer is to provide QA checks on legal descriptions prior to closing/condemnation
  Recommend using a plotting software such as Map98
    Map98 is free, and a tutorial video is available

## Slide 37: LEGAL DESCRIPTIONS
QA of Legal Descriptions should involve
  Checking the descriptions for closure
  Checking against the most current plans
    Revisions should be accounted for!
  Checking to see appropriate legal clauses are included and formatting follows the correct template
    Possible Examples:
      Demolition Easements
      Access Control Rights
      Uneconomic Remnants

## Slide 38: LEGAL DESCRIPTIONS
Controlled Access

## Slide 39: LEGAL DESCRIPTIONS
Uneconomic Remnants

## Slide 40: PLAN REVISIONS
ROW Engineer should review and document plan revisions as part of the project team.

## Slide 41: Example of Review Item
STUDY ACCESS MANAGEMENT

## Slide 42: Plan In Hand, PS&E
ROW Engineer should check the Plan in Hand and PS&E plans to ensure any revised items have been kept in the plan set.

## Slide 43: PROJECT DELIVERY NETWORK
Project Delivery Network (PDN)

## Slide 44: Excess Land Revisions
Revising plans per excess land sales as requested by the excess land coordinator.
Submitted to TDOT design file room.

## Slide 45: Questions?
Questions or Concerns?

## Slide 46: THANK YOU